## Slide 1: Combined effects of seismic directivity and attenuation: an example from surface microseismic monitoring
M. Wcislo (IRSM CAS, Charles University)
F. Staněk (Colorado School of Mines)
F. Gallovic (Charles University)
I. Pšenčík (IG CAS, Charles University)
S. Wu (IG Chinese Academy of Sciences)
APSLIM II &19th IWSA
Želiv, Czech Republic, 2022

## Slide 2: Outline
Motivation
Seismic directivity
Seismic attenuation and peak frequencies
Microseismic data
Combined effects of directivity and attenuation
Improvements in source mechanism inversion and interpretation

## Slide 3: Motivation
Cooperation with the Institute of Geology and Geophysics of the Chinese Academy of Sciences who shared a commercial field data acquired during hydraulic fracturing of shale in North China
Star-like surface array consists of 12 arms with 1780 1C geophones (vertical component) with recorded event availible
This type of data is not easy to aquire

## Slide 4: Motivation
Recordings of the obtained dataset included direct P-waves arrivals with high signal-to-noise ratio. They allowed us to investigate:
source mechanism of the event
frequency content (peak frequencies) of P-wave arrivals in relations to attenuation in the region and properties of the source.

## Slide 5: Rupture directivity of a seismic source
TR – rupture time
TAR - apparent rupture time
L – rupture lenght
α - an angle between the rupture direction and the direction to observer
VR – rupture velocity
V – seismic wave velocity (P or S)
M0 – seismic moment
TAR can be also expressed through:

## Slide 6: Seismic directivity
Approximate effect of directivity on amplitudes in comparison to S-wave
point source double couple radiation:
VP/VS ratio equal 1.7
VR=0.9VS
Point source
radiation pattern
Directivity effect on amplitudes
Radiation pattern with directivity effects

## Slide 7: Seismic directivity
Strong earthquakes – rupturę directivity has a significant effect on the directional distribution of seimic intensity
Small earthquakes (e.g., Pakor et al., 2016, Yoshida, 2019)
Microseismicity (Kane et al., 2013)
Acoustic emissions/Lab experiments (Kolář et al., 2020)
Directivity of microeartquakes may not be recorded due to the accumulated effect of attenuation on waveforms

## Slide 8: Seismic directivity & attenuation
A – non causal ray amplitudę at receiver
A0 – amplitude at the source
G – geometrical spreading, zxwR/T coefficients
t* - global absorption factor
Q – seismic quality
factor
r – ray point
t - traveltime
Waveforms close to the source
Waveforms after propagation through attenuative medium

## Slide 9: Seismic attenuation & peak frequency of the signal
Chart: Source displacement spectrum AD(f)
Flat displacement spectrum used in seismology corresponding to rectangular source time function. Corner frequency fC corresponds to the rupture duration
fC

## Slide 10
Chart: Source velocity spectrum
Chart: Attenuation effect: t*=0.01
Chart: Attenuated velocity spectrum
To find peak frequency we seek the maximum of the function:
The maximum of the function for f<fc :

## Slide 11: Seismic attenuation & peak frequency of the signal

## Slide 12: Measurement of peak frequencies
Examples of arrivals recorded by the array in China
Green brackets indicate the first half periods of the traces with clear arrivals

## Slide 13: Dataset - geometry
629 geophones provided clear, single direct arrivals (green dots)
Additional measurements of amplitudes for the mechanism computation (magenta dots)

## Slide 14: Results of peak frequency measurements

## Slide 15: Results of peak frequency measurements

## Slide 16: Differences in Q values – complexity of the medium?
no significant differences in traveltimes between arms
as example: red – arm 6, blue - arm 1

## Slide 17: Rupture directivity as an explanation of the peak frequency pattern?
Full moment tensor inversion using ray amplitudes
and point source approximation
Solution | Strike [deg] | Dip [deg] | Rake [deg]
Plane 1 | 326 | 85 | -180
Plane 2 | 236 | 90 | -5
Decomposition results | DC [%] | CLVD [%] | VOL [%]
 | 66 | 17 | 18
Map of recorded (circles) and modeled (squares) first amplitudes (blue negative, red positive)

## Slide 18: Seismic directivity combined with attenuation
To evaluate if combination of attenuation and directivity of the source may explain measured peak frequencies we performed synthetic modeling
Case 1: the peak frequencies are affected by neither attenuation nor the source directivity (best fit assumes a constant peak frequency).
Case 2: the attenuation is added to modeling (corner frequency of Brune spectra is limited up to 200Hz; a higher corner frequency is highly unlikely for MW ~1.0 event, Eisner et al. 2013).
Case 3: the effects of directivity calculated for the fixed VR/VS value of 0.9 are added.
Case 4: modeling with permitted supershear rupture propagation.

## Slide 19: Seismic directivity combined with attenuation
 |  |  | Tr | Q | Misfit | Misfit improvement | min / max modeled fpeak (logarithm)
No attenuation | No directivity | Vr/Vs=0 (fixed) | Not considered | Not considered | 36.6 | 1 | 48 (3,87) / 48 (3,87)
Attenuation |  | Vr/Vs=0 (fixed) | 1/200 s (fixed) | 150 | 18.1 | 2 | 37 (3,61) / 53 (3,95)
 | Directivity | Vr/Vs=0.9 (fixed) | 1/56 s | 220 | 13.7 | 2.7 | 35 (3,55) / 54 (3,98)
 |  | Vr/Vs=1.3 | 1/36 s | 200 | 11.8 | 3.1 | 31 (3,43) / 58 (4,06)
Measured: 29 (3.37) / 76 (4,33)
Measured (5% cut off): 33 (3.51) / 67 (4.20)

## Slide 20: Effect of seismic attenuation and rupture directivity

## Slide 21: Best fit subshear vs supershear
Search best fit: Vr/Vs=0.9 (fixed)
Global search best fit: Vr/Vs=1.3

## Slide 22: Directivity & source inversion
Distribution of ratios of real and modeled amplitudes reveal presence of the rupture directivity effects.
Linear fit of function of ratios of real and modeled amplitudes vs alfa angle is used to correct amplitudes for the rupture directivity effects

## Slide 23: Source inversion results – initial vs after correction
Original/Corrected
Maps of recorded (circles) and modeled (squares) first amplitudes (blue negative, red positive)
Original Corrected
Solution1/Solution2 | Strike [deg] | Dip [deg] | Rake [deg]
Plane 1 | 326/324 | 85/86 | -180/-178
Decomposition results | DC [%] | CLVD [%] | VOL [%]
 | 66/75 | 17/11 | 18/14

## Slide 24: Conclusions
Recorded peak frequencies can be explained by effects of rupture directivity and seismic attenuation
Rupture directivity allows determination of the true fault plane from the source mechanism solution
Star-like arrays provide good geometry for the stable source mechanism inversion

## Slide 25: Thank you for attention